|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 13 – C 1173 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | October 2011 |
|  |  | English only Original: English |
| Question(s): | 12/13 |  |
| STUDY GROUP 13 – CONTRIBUTION 1173 |
| Source: | ETRI |
| Title: | Revised Draft Recommendation Y.UbiNet-hn (Framework of object-to-object communication using ubiquitous networking) |

This contribution is the revised document of Draft Recommendation Y.UbiNet-hn based on the output document (TD 70 (IoT-GSI)) of IoT-GSI event held in Geneva on August 2011.

In this meeting, we would like to carefully review this revised text for the consent.

________________

Draft Recommendation Y.UbiNet-hn

Framework of object-to-object communication for ubiquitous networking

Summary

This draft Recommendation describes concept and high-level architectural model of object-to-object communication for ubiquitous networking and present several requirements and mechanism for identification of all objects and providing connectivity to them.

Keywords

Ubiquitous Networking, NGN, object

Contents

Pages

1.	Scope	4

2.	References	4

3.	Definitions	4

3.1	Terms defined elsewhere:	4

3.2	Terms defined in this Recommendation	5

4.	Abbreviations and acronyms	5

5.	Conventions	6

6. 	Ubiquitous networking in NGN	6

6.1	Overview of ubiquitous networking	6

6.2	Architectural model for ubiquitous networking	7

7. 	Basic concept of object-to-object communication	11

7.1	Objects in ubiquitous networking environment	11

7.2	Characteristics of objects	11

8. 	Requirements of “connecting to anything” capability for ubiquitous networking	13

8.1	General requirements for object-to-object communication	13

8.2	Technical considerations for object-to-object communication	14

9. 	A mechanism for object-to-object communication: identity processing for connecting to anything	16

10.	Security considerations	18

Appendix I Ubiquitous networking applications and examples using object-to-object communication	19

Draft Recommendation Y.UbiNet-hn

Framework of object-to-object communication for ubiquitous networking

# 1.	Scope

This draft Recommendation describes concept and high-level architectural model of object-to-object communication for ubiquitous networking in NGN and presents several requirements and mechanism for identification of all objects and providing connectivity to them. For this, this Recommendation covers the following:

- General overview of ubiquitous networking in NGN in the end-user perspective;

- Basic concept and high-level architectural model for object to object communication with NGN;

- Requirements and technical considerations of object-to-object communication for ubiquitous networking;

- A mechanism for object to object communication.

# 2.	References

The following ITU-T Recommendations and other references contain provisions, which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published.

The reference to a document within this Recommendation does not give it, as a stand-alone document, the status of a Recommendation.

[ITU-T Y.2001]		ITU-T Recommendation Y.2001 (2004), General overview of NGN

[ITU-T Y.2002]		ITU-T Draft Recommendation Y.2002 (2009), Overview of ubiquitous networking and of its support in NGN

[ITU-T Y.2011]		ITU-T Recommendation Y.2011 (2004), General principles and general reference model for Next Generation Networks

[ITU-T Y.2201]		Recommendation ITU-T Y.2201 (2009), Requirements and capabilities for ITU-T NGN.

[ITU-T Y.2291]		ITU-T Recommendation Y.2291 (2011), Architecture overview of next generation home network

[ITU-T Y.2701]		ITU-T Recommendation Y.2701 (2007), Security requirements for NGN release 1

[ITU-T Y.2702]		ITU-T Recommendation Y.2702 (2008), Authentication and authorization requirements for NGN release 1

# 3.	Definitions

## 3.1	Terms defined elsewhere:

This Recommendation uses the following terms defined elsewhere:

3.1.1	context [ITU-T Y.2002]: The information that can be used to characterize the environment of a user.

NOTE – Context information may include where the user is, what resources (devices, access points, noise level, bandwidth, etc) are near the user, at what time the user is moving, interaction history between person and objects, etc. According to specific applications, context information can be updated.

3.1.2	object [ITU-T Y.2002]: An intrinsic representation of an entity that is described at an appropriate level of abstraction in terms of its attributes and functions.

NOTE – An object is characterized by its behaviour. An object is distinct from any other object. An object interacts with its environment including other objects at its interaction points. An object is informally said to perform functions and offer services (an object which makes a function available is said to offer a service). For modelling purposes, these functions and services are specified in terms of the behaviour of the object and of its interfaces. An object can perform more than one function. A function can be performed by the cooperation of several objects.

NOTE – Objects include terminal devices (e.g. used by a person to access the network such as mobile phones, Personal computers, etc), remote monitoring devices (e.g. cameras, sensors, etc), information devices (e.g. content delivery server), products, contents, and resources.

3.1.3	ubiquitous networking [ITU-T Y.2002]: The ability for persons and/or devices  to access services and communicate while minimizing technical restrictions regarding where, when and how these services are accessed, in the context of the service(s) subscribed to.

NOTE – Although technical restrictions to access services and communicate may be minimized, other constraints such as regulatory, national, provider and environmental constraints may impose further restrictions.

## 3.2	Terms defined in this Recommendation

This Recommendation defines the following terms:

TBD

# 4.	Abbreviations and acronyms

This Recommendation uses the following abbreviations and acronyms:

API		Application Programming Interface

BT		Bio Technology

CT		Content Technology

IT		Information Technology

ITS		Intelligent Transportation System

NGN		Next Generation Network

NT		Nano Technology

PC		Personal Computer

PDA		Personal Digital Assistant

QoS		Quality of Service

QoE		Quality of Experience

RFID		Radio Frequency Identifier

# 5.	Conventions

In this Recommendation:

The keywords "is required to" indicate a requirement which must be strictly followed and from which no deviation is permitted, if conformance to this Recommendation is to be claimed.

The keywords "is prohibited from" indicate a requirement which must be strictly followed and from which no deviation is permitted, if conformance to this Recommendation is to be claimed.

The keywords "is recommended" indicate a requirement which is recommended but which is not absolutely required. Thus, this requirement need not be present to claim conformance.

The keywords "is not recommended" indicate a requirement which is not recommended but which is not specifically prohibited. Thus, conformance with this Recommendation can still be claimed even if this requirement is present.

The keywords "can optionally" indicate an optional requirement which is permissible, without implying any sense of being recommended. This term is not intended to imply that the vendor's implementation must provide the option, and the feature can be optionally enabled by the network operator/service provider. Rather, it means the vendor may optionally provide the feature and still claim conformance with this Recommendation.

# 6. 	Ubiquitous networking in NGN

## 6.1	Overview of ubiquitous networking

The term “ubiquitous networking” as defined in [ITU-T Y.2002] is used for networking capabilities to support various classes of applications/services which require “Any Services, Any Time, Any Where and Any Devices” operation using NGN enabled capabilities. This networking capability should support person-to-person, person-to-object (e.g., device and/or machine) and object-to-object communications.

For object-to-object communication, an object delivers information (e.g., sensor related information) to another object with or without the involvement of persons.

Figure 1 shows the general network configuration for ubiquitous networking. Objects around us are connected to the network and communicate independently establishing end to end connectivity. Objects which are not moving are called fixed objects. Objects which move from one place to another are called mobile objects. Logical objects (e.g., content in a server) are considered as an entity for providing connectivity. These objects are connected to NGN via wired or wireless interfaces in fixed environment (e.g., home, building) or mobile environment (e.g., vehicle).

Figure 1. General network configuration for ubiquitous networking

## 6.2	Architectural model for ubiquitous networking

From architectural model for ubiquitous networking in Figure 2, enhanced capabilities for ubiquitous networking in NGN are included:

- Connecting to anything;

- Web-based for ubiquitous services/applications;

- Context-aware and seamless capabilities;

- Multi-networking capabilities;

- End-to-end connectivity over interconnected networks.

Among the specified capabilities, “connecting to anything” is tightly related to functionalities in end-user side of NGN. In this draft Recommendation mainly focuses on object-to-object communication to support connecting to anything capability for ubiquitous networking in the end-user perspective.

Figure 2. Connecting to anything in architectural model for ubiquitous networking in NGN

Based on architectural model for ubiquitous networking in Figure 2, Figure 3 shows a high-level architectural model for object to object communication with NGN.

NOTE: H-TNI [ITU-T Y.2291] in end-user functions can be used for objects-to-object communication.

Figure 3. High-level architectural model for object to object communication with NGN

Capabilities for ubiquitous networking are highly distributed and interact with infrastructure (e.g., NGN) which interconnects with various types of objects (e.g., physical/logical/fixed/logical objects). The infrastructure aims to continuously capture, manage, and provide data about objects for applications. The following functions are required for object to object communication with NGN.

End-user functions

End-user functions provide a set of functionalities with or without gateway for connecting and collaborating objects in the end-user side. These functions can be any combination of the following categories:

- Information storage;

- Information collection;

- Information processing;

- Communication;

- Performing actions.

Depending on types of objects (see Section 7.2), objects which have limited functionalities collaborate among other objects to provide additional functionality. Additionally objects need unique identifiers or names that can be used as a link in order to find and manage data to support ubiquitous networking applications.

NGN transport stratum

Due to the heterogeneity of objects, in most cases a direct communication and data exchange between the objects is impossible. One of the functions of the transport stratum is to provide a bridge across this technological gap with end-user functions.

The transport stratum also supports the exchange of messages between the relevant set of objects and the given application. The transport stratum also maintains the list of objects and implements address mapping accordingly.

NGN service stratum

Usage context and situation of the objects are changed during the lifespan of the physical items. As objects move along the value chain, change owner and location, are faced with changing environmental and regulatory conditions, etc., the respective objects have to support different, often unpredictable, application scenarios. In close interaction with the transport stratum, the service stratum provides the required software repositories, as well as monitoring functionality to capture the current situation.

Function to establish highly available, scalable, and secure information management provides to automatically decide which portion of data is relevant in a given usage scenario and context.

The data that have been captured or processed at transport stratum have also to be filtered or aggregated carefully depending on the data density and accuracy required by the respective applications. Filtering and aggregation of data can be applied at multiple semantics levels.

To find the requested information that may reside in different data storage systems distributed all over the world, locally managed data repositories as well as a naming service are supported.

Ubiquitous networking applications

Ubiquitous networking applications utilize and enrich the information that the underlying infrastructure provides in many ways. Data that has been previously collected by objects and persisted in repositories are used to support various applications among various stakeholders.

NOTE: IdM functions and management functions are common functionalities to be considered both end-user side and NGN service/transport stratums.

# 7. 	Basic concept of object-to-object communication

## 7.1	Objects in ubiquitous networking environment

The object means the user or other entity which is connected to the network. It includes almost everything around us such as remote monitoring and information device/machine/content, etc.

As shown in Figure 4, the types of objects in end-user side include the following:

- Personal devices;

- Information devices;

- RFID/sensors;

- Contents;

- Appliances;

- Vehicles, etc.

Figure 4. Conceptual diagram for “connecting to anything” with NGN

## 7.2	Characteristics of objects

Objects can be classified into several types as follows.

- Physical object vs. logical object (e.g., content, resource, etc)

- Mobility: fixed object vs. mobile object

- Tag: Active RFID vs. Passive RFID

- Size: common(normal) devices vs. tiny(small) devices

- Power/energy: power supplied vs. power limited (for emergency)

- Manageability: managed by human vs. managed by device human intervened or not

- Different networking capabilities: IP vs. non-IP, etc

  - In most cases, an unattended (constrained) devices communicating with others objects in a potentially very large scale environment

Objects in ubiquitous networking environment have the following characteristics.

- Heterogamous access interfaces

- Lightweight protocol for low power consumption

- Different amount of information transactions

Table 1 shows characteristics and examples of each type of objects according to the classification of objects. These objects are characterized by the following heterogeneities: order(s) of magnitude bigger than the Internet, no computers or humans at endpoint, inherently mobile, disconnected, unattended object and communication style and so on.

Table I. Characteristics and examples of objects in ubiquitous networking environment

| Types | Characteristics | Examples |
| --- | --- | --- |
| Size | Small objects | Small in size, short communication range | Sensor, tiny devices |
|  | Normal objects | No constraint in size | Home appliances |
| Mobility | Mobile objects | Moveable, continuous change in context information | Car, bus, and train |
|  | Fixed objects | Do not move normally and can be connected to electrical power | Traffic light, building, bridge |
| Power | Objects without power supply | Do not have continuous power, battery with fixed period of uses | Sensor in outdoor, RFID |
|  | Objects with power supply | Connected with power supply, no need to be worried about energy consumption | Home appliances |
| Connectivity | Objects connected to physical world | Objects are connected to physical world to provide data and information about some real time phenomenon. Objects are not only able to sense physical information but also able to react according to need. | Environment sensors (measuring temperature, pressure, humidity, rain etc) Actuators, robots, automatic application triggering depend on context information |
|  | Intermittent connectivity | Objects communicate and collaborate intermittently (periodically or based on some contextual condition) | Sensor which sends data in every pre-defined time interval Actuator or robot which act according to its surrounding: increasing, lowering temperature, calling security, fire or emergency services based on environmental conditions |
| Ability | Ability to sense and actuate | Object sense the environment where it is subjected. Object can also react based on sensed information. | Normal sensors, actuators (senses and react dynamically) [NOTE] |
| People involvement | Object of interest of people | People can augment communication and computation properties on the physical objects. | Tagged food item, electric lamp with light sensor, video content with automatically pause and play capabilities, cup with thermometer |
|  | Objects managed by devices not people | These objects are managed by other devices rather than people themselves. | Smart meter managing light sensors around home, Home automation system managing automatic door and windows system. |
| Physical/ logical | Physical objects | All physical objects related to real time activities falls in this category. | Different sensors attached with physical objects (lamp, environment, tree etc) |
|  | Logical objects | Can be identified as a resource or a virtual object by using a unique identifier | Contents and resources (e.g., software, computing power, storage) |
| Object with tag | Object with active tag | Object can be tagged with active RFID tag. | Products attached with active RFID |
|  | Object with passive tag | Passive tag can be attached with objects which need to be uniquely identified. | Items tagged with passive RFID in shipping company, supermarket |
| IP/ Non IP | IP enabled object | IP enabled objects are capable of having end to end connectivity. | Refrigerator in home which has own IP address, TV, electric lap with processing devices |
|  | Non IP enabled object | Non IP enabled objects participate in network with the help of some gateway or middleware which acts on behalf of the objects. | Non IP objects: tiny devices, products with active or passive RFID tag |

NOTE: Classification according to different roles/names can be considered as follows.

- A sensor: device that measures a physical quantity and converts it to analog or digital signal: power consumption and quality, vibration of an engine, pollution, temperature, CO, motion detection, temperature, etc

- An actuator: device that controls a set of equipment (e.g. control and/or modulates the flow of a gas or liquid, control electricity distribution, perform a mechanical operation)

# 8. 	Requirements of “connecting to anything” capability for ubiquitous networking

## 8.1	General requirements for object-to-object communication

For object to object communications, suitable medium to connect to each other is required to get benefits of always anywhere and anything communications. Intelligence of objects helps to reduce the load into the whole system. Processing can be done towards the edge of the network. Network component should be small enough so that it can be mounted in all the things. The following are general requirements for communications between objects in NGN.

- Size, power, and capability of the communication objects are less compare to high processing computing devices. To cope with those limited capabilities, it is required to use lightweight protocols.

  - As current Internet protocols have high payload and control information, it is required to optimize communication layers to add required functionalities and remove unnecessary loads.

- For configuring objects manually or semi manually, it is required to provide autonomous and self configuration and network adaptation functionality.

- Auto discovery is required to connect any objects which are in the range of communication. Objects are required to get all the required parameters they need when they are connected to the network.

- Mobility of the communicating objects should be addressed. Object can move from one place to another and may attach with another network with different technology. Object mobility management is required to provide seamless communication among automated objects.

- Size of routing table becomes large because of millions of communicating objects. It is required to support optimized and dynamic routing.

- Network size is increasing as a lot of objects are connected into the network. Scalability is required to be handled to incorporate more and more communicating objects.

- Each communicating objects should be able to create end to end connectivity with each other. To get end to end connectivity, each object is recommended to have separate unique IP address. Enough address should be there to allocate large number of objects connecting to the network. Otherwise, each object should provide the direct connectivity to host with a unique IP address.

- Programming platform is required so that applications can be developed quickly and easily.

- It is required to provide QoS and QoE of required level. Important objects need to handle on time and with some level of accuracy.

- There are many security and privacy issues in current Internet which should not be present in ubiquitous networking environments as it is connecting many sophisticated objects which might cause huge damage if its security is breached. Security and privacy are required to be managed with proper way.

- Communication errors are required to be detected and corrected.

## 8.2	Technical considerations for object-to-object communication

Technical considerations for object-to-object communication of ubiquitous networking are as follows:

Scalability

In ubiquitous networking environment, there are small (home environment) or large scale (factory, shopping mall) environment in end-user domain. Objects communicate with each other and with people seamlessly. Each constituent is offering different services. Basic functionalities such as communication, service discovery are required to be functioning efficiently in both small and large scale environment.

Scalability regarding addressing can be taken as an example. Object-to-object communication needs huge number of IP addresses in order to uniquely identify each object. As a scalable solution, IPv6 can optionally be used which can accommodate as many objects as required to include in ubiquitous networking.

Interoperability

Objects have different communication, information and processing capabilities. Each object is also subjected to very different conditions such as power energy availability and communication bandwidth requirement. Interoperability issue includes heterogeneities of device, services.

Interoperability solution is required to be maintained to provide seamless interaction among objects. Service description, publishing, and discovery mechanisms is required to be interoperable, otherwise additional networking capabilities is required to be provided for supporting islands of objects in heterogeneous networks.

Discovery

In dynamic environment of ubiquitous networking, suitable services for objects must be automatically identified. It is required to support appropriate semantic means of describing their functionality. For example, users want to know product information and their availability all the time.

Self-configuration is required for each object to configure itself without manual/human intervention. For this, context information has critical roles to support context aware networking for changes of communication environments and support semantic as the virtual representation of physical objects.

Data volumes

Depending on application and use cases there is vary in data volume. If there are a large number of peer objects communicating with each other, an object runs out of processing, memory and storage. From network perspective, it is difficult to handle bulk amount of data if objects produce huge bytes of data regularly.

To solve this problem, it is required to develop solutions such as periodic communication between objects, data compression and optimized traffic engineering.

Power supply

As objects move around, it is difficult to connect to power supply all the time. So they need to operate with self-sufficient energy source. It is required to develop energy efficient protocols for minimizing power consumption and eliminating unnecessary communication procedure among objects.

Fault-tolerance

To maintain robust and trust worthy, dynamic ubiquitous networking environment is required to support redundancy in several levels and ability in order to automatically adapt to changed and/or abnormal conditions.

Security and personal privacy

Confidentiality, authenticity and trustworthiness of communication partners are required to be maintained. Users may want to give objects limited service access not allowing them to communicate in uncontrolled manner.

Intelligence

The objects is required to intelligently cooperate with their environment. Sensing current environment, acting intelligently according to situation is required to support services using object-to-object communication.

Objects act according to their predetermined set of actions or they collaborate with each other based on current context and act accordingly.

There are heterogeneous devices, application scenarios, data format, and communication network. Each connected object is required to adapt networking environment where it is now.

# 9. 	A mechanism for object-to-object communication: identity processing for connecting to anything

Instead of existing network terminals, new types of devices such as RFID, sensors, smart cards, etc lead the change for the ubiquitous networking which enables devices to communicate between themselves. Identification, naming, and addressing capabilities are essential for supporting ‘connecting to anything’ in end-user domain.

To support connecting to anything, there are specific technical considerations for connecting to anything through considering the following points:

- Identification of object(s);

- Finding/tracking  the location of object(s);

- Provide  connectivity to the NGN in cooperation with naming and addressing;

- Specific use cases for fusion services combined with other industries.

In ubiquitous networking, for object to object communications, information for several kinds of object on top of end points should be identified in the network. A service is an entity that is either an instance of a specific application service or a specific data object. The identity of the object persists over time and is not tied to the end system hosting the service or data.

Identification of all objects for providing end-to-end connectivity in ubiquitous networking environment is crucial. Identifier(s) in ubiquitous networking is capable enough of identifying all relevant objects and facilitating object-to-object communications. In particular, the globally unique identifier(s) enable a great many applications including tracking, access control, and protection of objects, etc.

As shown in Figure 5, the layered architecture of NGN requires specific processing capabilities at each layer. Each user/object in applications identifies by identity like name with a set of attributes of an entity. An attribute can be thought of as metadata that belongs to a specific entity in a specific context, some of which could to be highly private or sensitive. The identity should be associated with object IDs (RFID, content ID, telephone number, URI/URL, etc) through identification and authorization. Each object ID also should be associated with communication IDs (session/protocol ID, IP address, MAC address, etc) through mapping/binding.

Figure 5. Identity processing for connecting to anything

All of devices (i.e., objects) should be reachable to the other users/devices. Since managing a large number of different identification codes to use IP network infrastructure becomes vital, it is very important to use both location information of IP address and uniqueness information of identification codes.

For connecting to anything using object identification, the Figure 6 shows object mapping/binding with IP address for IP connectivity to all objects in end-user side. It provides the global connectivity with NGN to objects through the association (e.g., mapping/binding) between identifier for object and IP address.

Figure 6. Object mapping/binding with IP address for connecting to anything

# 10.	Security considerations

Basic considerations on security architecture for NGN are addressed in [ITU-T Y.2001] while security requirements of the NGN are described in [ITU-T Y.2701]. Concerning the specifics of ubiquitous networking, the various kinds of terminals, devices and contents that can be involved will have to conform to the security requirements of the network they are willing to attach. When attaching to the NGN, corresponding authentication and authorization requirements as described in [ITU-T Y.2702].

In this Recommendation, objects involved in NGN have their own identities and are interconnected involving more interactions throughout a dynamic and heterogeneous environment. Accordingly, security including the design of the security architecture for a secure information discovery and delivery to users including persons and objects is very crucial.

# Appendix I
Ubiquitous networking applications and examples using object-to-object communication

(This appendix does not form an integral part of this Recommendation)

In ubiquitous networking environment, applications can be newly created through the integration and combination of technologies such as BT, NT, CT, etc. Therefore, it is necessary to combine BT, NT, CT as well as IT using ubiquitous networking capabilities.

Communication networks have been mainly supporting the evolution of information processing and service capabilities within IT industries. However, the capabilities of networks benefiting from ubiquitous networking should impact other industries such as medical industry, education industry, finance industry, transportation/distribution industry, etc., resulting in new requirements for specific services taking into consideration of IT technologies.

Figure II-1. Examples of Ubiquitous networking applications

As shown in Figure II-1, the technologies using connecting to anything can be used for the following applications/services in the convergence environment with IT:

- IT + transportation: ITS, networked vehicle and telematics, navigation etc

- IT + education: online cyber learning system

- IT + building: IBS, home networking, etc

- IT + supply chain: supply chain management, distribution system, etc

- IT + health: remote diagnosis and medical experimentation, etc

- IT + life: environment management, equipment management, etc

- IT + disaster: disaster management, emergency alarming system, etc

- IT + safety: finance, commerce, public peace, etc

For supporting ubiquitous networking applications, NGN shall solve technical considerations which are specified in Section 8.

________________